## Slide 1: Network Services Interface Network Engineering Tutorial
Presented at TIP 2013
Jan 13, 2013
Honolulu, HI

## Slide 2: Today’s Objectives:
Explain the Network Services Interface
Provide a network engineer’s perspective on deployment planning
Provide hands on experience constructing NSI services

## Slide 3: Presenters:
Inder Monga Dir, Research Programs, Esnet imonga@es.net
Tomohiro Kudoh Sr. Research Scientist/Group Leader, AIST t.kudoh@aist.go.jp
Jeroen van der Ham Research Scientist, University of Amsterdam
Jerry Sobieski Dir, Int’l Reserearch Initiatives, NORDUnet jerry@nordu.net

## Slide 4: Schedule
8:30-8:40 Introductions (Jerry Sobieski)
8:40-9:15 Connection Oriented Services Concepts (Inder Monga)
9:15- 10:00 The NSI Framework and CS Protocol (Jerry Sobieski)
10:00-11:00 Exercise #1 Basic Connection Life Cycle
Break (In conjunction with Exer#1)
11:00-11:45 NSI-CS Protocol State Machine, and MDL (Tomohiro Kudoh)
11:45-12:00 A Peek at the NSI software WSDL (Inder Monga)
12:00-12:30 Lunch
12:30-1:30 Exercise #2 Multi-Domain Provisioning
1:30-2:15 Advanced Topology – NML & N3 (Jeroen van der Ham)
2:15- 3:15 Exercise #3 Topology Development
Break (in conjunction with Exer. #3)
3:15-4:00 Putting it together - Deployment Planning (Jerry Sobieski)
4:00-4:15 GLIF Automated GOLE (Jerry Sobieski)
4:15-4:30 Discussion and Close (all)

## Slide 5: Set the Stage: NSI in a slide
“Network Service Interface” is a framework for inter-domain provisioning of connection-oriented services.
NSI is an Open Grid Forum (OGF) standard
NSI is a consensus standard – open to wide participation and broad based agreement.
It is a work in progress. …and will continue to be evolve and be refined.
As a framework, NSI is intended to provide a scalable, secure, and well integrated set of multi-domain architectural elements and service protocols that manage all aspects of services they present:
  Connection Reservation and Provisioning: NSI-CS (version2 – 2012)
  Topology Exchange (first edition expected in 2013)
  Others in the wings:
    Automated Performance Verification
    Automated Fault Processing

## Slide 6: Introduction Connection Oriented Service Concepts
What are they? Why are these different from conventional IP services?
Why do we need them? (Best effort vs. performance guarantees)
Where/when are they appropriate? …primary use cases: data intensive science, scheduling, emerging virtualization environments
How do they work? generic details – packet oriented, spectrum oriented, signaling, path finding, etc.
Inder Monga – Research Director for Esnet at LBL, Co-Chair of NSI-WG and GLIF NSI Implementation Task Force, formerly with NORTEL. Generally smart guy – listen to him.

## Slide 7: INDER’s Slides

## Slide 8: Introduction NSI – The Network Services Interface
What is the NSI “Framework”
Details on the NSI “Connection Service” protocol
* Jerry Sobieski NORDUnet Director for Int’l Research, TL for the GLIF AutoGOLE Pilot, co-Chair of GLIF Performance Verification Architecture Task Force, formerly with MAX (US)
Begin Jerry’s Slides

## Slide 9: Why is NSI different?
NSI represents a consensus approach to inter-domain provisioning of Connection Services
  It has patiently worked through the religion to find agreement among diverse perspectives
It is an open standard –
  It allows anyone to participate in the process …it is not dominated by the interests of a few prominent organizations.
  The standards effort includes network theorists, experienced network operations and engineering personnel, knowledgeable users/developers, computer scientists/researchers, etc.
An open consensus standard creates “buy-in”
  Since everyone has had a voice in its specification, and understands its workings, everyone is willing to adopt it and deploy it
Leads to Ubiquity –the same interfaces and capabilities are available everywhere.

## Slide 10: NSI Features
NSI is a framework with numerous service capabilities and a simple scalable network model.
NSI is an inter-domain set of protocols
    It does not deal with intra-domain construction/issues
NSI is technology agnostic
    It builds simple atomic transport conduits according to the services defined by the community (not fixed in the protocol)
NSI connection services are highly customizable
    NSI Service Definitions can support a wide range of services
NSI is secure by design
    All requests are authorized at domain boundaries according to local and/or voluntary policy rules and security profiles

## Slide 11: The Network Services Interface
NSI adopts a simple peer model of “Requester” and “Provider” agents for all service primitives
  NSI protocols treat all network service agents the same - no longer differentiating “user” vs “network” or “client” vs “server”…
Treating all agents the same means we must provide an interface that can be both very simple for basic user adoption yet has the ability to offer very sophisticated functionality for network service providers
Requesting Agent (RA)
Provider Agent (PA)
Network Services Interface
Protocol(s)
NSA
NSA

## Slide 12: The Network Services Interface
NSI poses a generic notion of a “connection” as an atomic service element – a generalized logical conduit for data transport
  Abstract Ingress and Egress end points
  Abstracted transport service between the end points
NSI also poses a simple inter-domain architecture over which connections are allocated
Ingress interface
Egress interface
“Aruba”
A
C
B
“Bonaire”
J
K
L
User data
Transport

## Slide 13: NSI Framework Overview
The “NSI Framework” describes a scalable multi-domain network architecture for connection services
NSI incorporates a comprehensive set of integrated protocols that work together to support end-to-end connection services
Connection
Service
Discovery
Service
Topology
Service
Performance Verification
Service
…
Service
Network Services Interface Framework
Topology, Services, Agents, Protocols

## Slide 14: NSI Framework Overview
  NSI specifies an abstract model of a network “Connection”
  NSI specifies an abstract global “Topology” model over which Connections are established
  NSI specifies an abstract notion of “Service Termination Points” – the Connection end points
  NSI specifies abstracted “Network Service Agents” (NSA) that represent each NSI service domain and implement the NSI protocol(s)
  NSI specifies the high level protocol(s) between NSAs that enable global inter-domain service management.

## Slide 15: NSI: A Basic Overview:
NSI protocol(s)
C
Domain C
B
Requesting
Agent (RA)
Network Resource Manager
Provider
Agent (PA)
NRM
Network Services Interface
Protocol(s)
NSA
Network Services Agent (NSA)
NSA
NSI “Network Service”
Domain B
Domain A
A
Application NSA
NSI Topology

## Slide 16: The NSI Connection
An NSI Connection is defined as:
  A logical conduit between two network locations through which user information is carried transparently and unmodified from the ingress location to the egress location.
  Connections are generic point to point pipes across network service domains
  A Connection is established across an NSI Network between two “endpoints” at the edge of that network.
“Bonaire”
“Aruba”
A
C
B
J
L
K
NSI Connections:
“Curacao”
X
Z
Y
A > B
J > K
X > Z

## Slide 17: The NSI Topology
“Curacao”
The basic NSI Topology describes a global set of interconnected Network Service domains
  Autonomous network service domains: “NSI Networks”
  Service Termination Points “STPs” define the operational/administrative boundary of a network service domain
  And relations called Service Demarcation Points “SDPs” that define adjacencies among NSI networks.
“Bonaire”
“Aruba”
A
C
B
J
L
K
NSI Networks
X
Z
Y
NSI Service Termination Points
NSI Service Demarcation Points

## Slide 18: Adjacency
“Aruba”
“Bonaire”
“Curacao”
Service Demarcation Points, “SDP”s, describe how NSI service domains are interconnected
  SDPs indicate where two NSI service domains are “adjacent”
  Thus, an SDP is a pairing of an STP in one network with a corresponding STP in another network. For example
    Aruba:B == Bonaire:J or Bonaire:K == Curacao:X
  The STPs in an SDP pairing are topologically equivalent – i.e. each STP references the same interface between networks – but using different names
A
C
B
J
L
K
X
Z
Y
NSI Service Demarcation Points
SDP B==J
SDP K==X

## Slide 19: Service Termination Points
In NSI an “endpoint” is conceptually a dimensionless interface at the edge of a network – it is a hole at the boundary of a network through which user data enters or exits that network
  In the context of the inter-domain topology, an endpoint is a topological location where a particular NSI Connection may originate or terminate,
  In the context of the intra-domain topology, the STP represents the internal specifications that uniquely identify the data entering or exiting a specific connection and distinguish that data from all other user data transiting the boundary of the local network service domain.
These are the terminals for connections, so they are formally referenced as “Service Termination Points” (STP)
A conceptual model of the connection conduit between A and B: A>B
Ingress
STP A
Egress
STP B
Network “Aruba”
A
C
B
Endpoints
“Service Termination
Points”
Notes: An endpoint is *NOT* a physical location – it is a topological location… i.e. the model allows virtualized topologies.
Connections do not share endpoints – this would break rule 2b (differentiation)

## Slide 20: STP Identifiers
An STP Identifier is a symbolic name – it serves only to identify a unique endpoint globally without expressing any [intra-domain] technical specifics about the endpoint
An NSI STP Identifier consists of two parts:
  <networkID> : <localID>
  The networkID is the NSI Network in which the STP resides,
  The localID identifies the STP within that network
  Ex: Aruba : A1 or: Nordunet : CPH1-ge-0-3-1780
  NSI Network IDs are required to be globally unique
  Local IDs must be unique within the scope of their NSI Network.
The only relevant NSI information carried by an STP Identifier is the network in which it resides
  Which is [really] all NSI inter-domain path planning needs to know
Notes: From a provider’s standpoint, we can not question the RA’s choice of endpoints or the basis for why/how the RA selected the end points for the connection request. Nor can we presume to know anything more about the purpose or requirements of the request other than what is explicitly expressed in the request itself.
The PA now has the A and Z endpoints that it must connect, and must do so with the topology information it has at hand (or can acquire) and its own topology analysis capabilities within its own path finder.
Presumeably, the ultimate Requester

## Slide 21: STP “2-tuple” Identifiers
STP 2-tuple Identifier contains enough information in their name to associate the end points with their networks.
  This is sufficient to allow the NSI agents to perform inter-domain path finding.
  The localID is only used by the first/last hop networks for the intra-domain path planning
The local NRM translates a localID portion of the STP Identifier to the local private topological information necessary to provision the connection. For example:
NetworkId “aruba”:
Local ID Switch port Qtag QinQ Remote
A100 cph1 g10 100 - -
A101 cph1 g12 101 - aruba:Port3-80
Port3-80 192.168.1.151 g3 1780 - aruba:A101
Port24-99 192.168.1.151 g24 1799 200 aruba:Port4-z
Bonaire81 cph1 g3 1781 - bonaire:p3-12
Cust-Acme nyc1 g9 - - -
Port4-z nyc1 g4 1799 - aruba:port24-99

## Slide 22: STP References and Type Value Pairs
STPs can be referenced using “type value pairs”:
  A TV Pair contains a “type” identifier, and a value for that type.
  E.g. a STP identifier can be referenced using TVP syntax:
  NetworkID=“ets.nordu.net”, LocalId=“ams80”
TV pairs allow us to reference STPs using either the abstract NSI symbolic identifiers, or to describe an endpoint using more detailed technical information [if known]:
  NetworkID=“ets.nordu.net”, region=“denmark”, node=“cph1”, port=“ge2-3”, vlan=“1780” ;
  A fully specified NML topological “n-tuple” reference in TVP form:
  Topology=“urn:ogf:network:ets.nordu.net:2012:topology”, BiDirectionalPort=“urn:ogf:network:ets.nordu.net:2012:g3”, vlan=“1799”;

## Slide 23: Anatomy of a NSI “Connection”
The STP framing defines how the user payload is presented across the inter-domain boundary (i.e. at the ingress [or egress] point).
The Service Definition defines the service payload that is carried from the ingress STP across the transport section and presented at the egress STP.
    Note- the Service Def does not define the internal “switching” technology! This is left to the local engineers…
  STPs and Connections can be either uni-directional or bi-directional
    The Connection mode is specified in the Reservation request
    While it is not strictly required, it is recommended to match like elements, as mixed mode requests may produce unpredictable service instances
Ingress
Service Termination Point
“A”
Egress
Service Termination Point
“Z”
Transport section
Access section
Access section
Egress
Framing
Ingress
Framing

## Slide 24: NSI Connection Service
An NSI Network represents a “Connection Service”.
    The boundary edge of a NSI Network domain is defined by the service termination points that the service is able to cross-connect.
The network switching model is that of a simple non-blocking cross-connect: “any endpoint can be connected to any other endpoint, if resources are available.”
    By default, NSI networks hide all internal topology from external agents.
    How the cross-connect is accomplished is [strictly speaking] a local internal issue only.
    Note: Opaque networks is a default strategy that errs on the side of security and privacy…Networks may expose more if they wish… see NML.
“Bonaire”
“Aruba”
A
C
B
X
Z
Y

## Slide 25: Path Finding and Connection Segmentation
NSI is an inter-domain framework. Thus it’s primary path selection objective is to select a viable inter-domain path that meets the requested Connection criteria
  Each Connection is decomposed recursively to a sequence of single-domain Connection “segments” – each segment is comprised of SDP end points at the inter-domain boundaries
  The segments, when concatenated, form the end to end Connection instance.
  Example: The end-to-end request Aruba:A > Curacao:Z is segmented into:
  (Aruba:A > Aruba:B), (Bonaire:J > Bonaire:K), (Curacao:X > Curacao:Z)
“Bonaire”
“Aruba”
A
C
B
J
L
K
“Curacao”
X
Z
Y
Aruba:A > Aruba:B
Bonaire:J > Bonaire:K
Curacao:X > Curacao:Z
(Aruba:B == Bonaire:J)
SDP B==J
SDP K==X
(Bonaire:K==Curacao:X)

## Slide 26: Segmentation and end-to-end Connections
Ingress
Service Termination Point
“A”
Egress
Service Termination Point
“B”
Transport
Access
Access
Ingress STP
“J”
Egress STP
“K”
Transport
Access
Access
Transport
Segment 2
J
K
A
B
Transport
Segment 1
Access
B==J
A>J
J>K
Access
A>B
STP A
STP B
STP J
STP K
J>K
B==J
“Bonaire”
“Aruba”
A
C
B
J
K
L

## Slide 27: NSI Network Adjacency
Since SDPs indicate where two STPs identify the same inter-domain interface, the STPs themselves must have matching characteristics.
  I.e. all aspects of an STP must be the same (e.g. framing type, MTU, etc.) in both networks.
  By extension then, if network Aruba can connect any STP in its domain to STP J, and network Bonaire can connect K to any other STP in its domain, then by concatenation, a connection can be made between any STP in Aruba and any STP in Bonaire as long as transit SDPs and/or other necessary internal resources are available.
  Thus Aruba and Bonaire form a common service region.
“Bonaire”
“Aruba”
A
B
J
K
Y
Z

## Slide 28: Constructing the NSI Topology Model
Bonaire
Aruba
P0
X0
P1
L1
X1
P0
P2
P1
P2
P0
X0
P1
L1
X1
P1
P2
P0
P2
P4
P5
Bonaire
Aruba
The NSI model explicitly assigns authoritative ownership of all physical components to one network or the other.
Conventional physical infrastructure –
Networks, switches, ports, and links
The physical topology is translated to a derivative “resource graph” consisting solely of Resources, logical resource Interfaces, and Adjacency relations
Technology agnostic inter-domain Service Termination Points (“STP”s) are defined and mapped logically to internal physical components. External relations are NSI Service Demarcation Points (“SDP”s).
Bonaire
Aruba
Bonaire:B1
Aruba:A0
Aruba:A1
Bonaire:B0
STP
Bonaire:B2
STP
Aruba:A2
SDP
By hiding all internal structure and only exposing inter-domain STPs and their peering SDP relations, we arrive at the basic NSI Topology Model of networks, STPs, and the SDPs that indicate inter-domain adjacency.
P1
X1
P0
P2
P0
X0
P1
P2
Bonaire
Aruba
L1
B1
A0
A1
B0
B2
A2
P5
P4

## Slide 29: OGF Network Markup Language
Connection Services require path finders to explore the global network and select a viable end-to-end path for each connection request
The path finders require a “topological” view of the world to do this – a topology DB
Global topology management is necessarily a globally distributed process
In order for distributed agents (NSAs) to exchange topology information, they must share a common topology representation and a common descriptive exchange format.
NSI supports the OGF Network Markup Language for inter-domain topology representation and expression.
NSI uses the N3 syntactical form of NDL to describe the NML topology information
  More on NML and N3 this afternoon

## Slide 30: NSI Topology Issues
Detailed Internal Topology descriptions
  NSI specifies a very simple – but highly scalable - inter-domain topological model…
  This is one end of a spectrum… while full visibility to detailed topology state in a global network is intractable…we can nevertheless provide more detail than…nothing.
  NSI can co-exist with much more detailed topology and path specifications.
NSI(v2) stipulates the OGF Network Markup Language for topology specifications –
  the NSI topological model is described within the NML ontology and specification.
  An NSI Connection request can specify STPs that exist “within” an NSI service domain: Explicit Route Objects
  (This is new feature in v2 and depends upon networks announcing internal details, and requesting agents having sophisticated path finders that understand the detailed topology.)

## Slide 31: Pt to Any Pt STP “n-tuple” References
Type Value Pair syntax can be used where some detailed aspect(s) of the STPs are known or desired by the RA and/or other aspects are left to be specified by the PA.
  For instance: A Connection is to terminate at an end system, but the specific VLANID is flexible: Ex:
Topology=urn:ogf:network:netherlight.net:2012:nsi-topo:p2pcs, BidirectionalPort=urn:ogf:network:netherlight.net:2012:topo:p2pcs:ams1-te-0-0,
Vlanid=“1780-1799”;
Thus, networks THAT CHOOSE TO can expose substantially more internal infrastructure detail and state to external agents
  And users can specify a more detailed path using the NML objects (See exercise 3)

## Slide 32: NSI + NML Topology
NSI topology is augmented by the OGF Network Markup Language (NML)
NML allows a NSI network to announce additional detail about internal topology – if/when they choose to do so.
Topological information is required for many purposes – NSI-CS is just one (e.g. performance verification, or fault analysis)
  Note: NML was not defined as part of NSI – but was adapted to work appropriately within the NSI environment…some inconsistencies still remain to be worked out.
We will cover NML after lunch in detail
Notes: NSI – NML inconsistencies: NML expects all topo objects to have a globally unique name… since the NSI STP maps to an NML *port, and the NML requires a port to have a GUID, then NML local ids will have GUIDs..

## Slide 33: NSI is Technology Agnostic
NRM
NRM
NRM
NRM
  NSI views a Connection from a service perspective – not from the hardware plumbing perspective.
    Connections are generic “pipes” - not VLANs, or SONET/SDH circuits, or LSPs…
  NSI does not specify transport technologies used within each domain
    Each network decides their own internal transport engineering
    The Network Resource Manager handles internal provisioning
NSI is therefore highly amenable to multi-layer, multi-domain, multi-service data transport environments -> i.e. modern networks.
NSA
NSA
NSA
NSA
Ethernet
MPLS
Waves
SDN

## Slide 34: “Technology Agnostic”
NSI framework and protocols deal with high level abstract constructs: “services”, “connections”, “termination points”…
The NSI protocol standards do not define service specific parameters - such as “Bandwidth”, or “Frame Error Rate”
These are service specific transport parameters, and are defined as part of the “Service Definition”
This allows the service providers to change or create services without needing to change the protocol
NSI leaves technology specific engineering to the network engineers.
NSI standard also does not specify or assume technology specifics for Service Termination Points – these too are service specific.

## Slide 35: NSI Protocols
Relative to any “Network Service” process, the NSI protocol agents participating in the process assume one of two roles:
  Requesting Agent (“RA”) – any agent that formulates a service request presents it to another agent
  Provider Agent (“PA”) – an agent that receives a request and acts to provide the requested service.
Requesting
Agent (RA)
Provider
Agent (PA)
Network Services Interface
Protocol(s)
NSA
Network Services Agents
NSA

## Slide 36: NSI Connection Service Protocol
The first protocol standardized within the NSI Framework is the Connection Service protocol: “NSI-CS”
  NSI-CS manages a NSI Connection though its entire life cycle from inception to final completion.
NSI-CS is [currently] defined as a “Web Service.”
  This is largely an aspect that governs inter-agent communication – not the high level protocol itself
The WSDL can be found at:
  http://code.google.com/p/ogf-nsi-project/source/checkout
  https://code.google.com/p/ogf-nsi-project/source/browse/#svn%2Ftrunk

## Slide 37: Basic NSI-CS Connection Life Cycle
reserving
provisioning
releasing
terminating
released
In-service
scheduled
The NSI-CS protocol primitives are “request/response” pairs:
  Each primitive is issued as a message from one agent to another
  Primitives requests originate with a Requesting Agent (RA) and are sent to the Provider Agent (PA)
  The PA issues a corresponding response (confirmed or fail) back to the RA.
  Each NSA manages a state table associated with each Connection it is servicing.
The CS protocol is designed to provide consistent life cycle state transitions for NSI connection instances regardless of how they are segmented
RA
PA
Resv.rq
Resv.cf
Prov.rq
Prov.cf
…
…
…
…
Rel.rq
Rel.cf
Term.rq
Term.cf

## Slide 38: Basic NSI-CS Primitives:
Reserve:
  Requests that a Connection instance be created, and resources reserved, that meet the performance requirements specified by the requesting agent.
Provision:
  Causes the resources allocated to a Connection to be configured to allow the transport of user traffic. Puts the Connection into service.
Release:
  Reconfigures the hardware to prevent the flow of user traffic. Takes the Connection out of service
  Resources are retained so that the Connection can be re-Provisioned at a later time
Terminate:
  Releases the Connection if still in-service, frees all resources that were reserved for the Connection.

## Slide 39: Special Primitives:
Query: Two forms
  Basic: Takes a Connection ID and returns the “as buit” information that would be returned to the RA in a Reserve Confirm.
  Detailed: The PA walks the service tree performing Queries on its children and returns the whole service tree.
Notify:
  This is the only CS primitive that goes from the PA to the RA.
  It is used to notify RAs of surprises (error conditions).
Modify:
  Change the reservation characteristics (e.g. bandwidth, end time, etc.)

## Slide 40: NSI Reservation Request
A NSI-CS Reservation request specifies:
  Global ID – option tag used for correlating segments
  NSI Connection ID - RA assigned connection ID
  Description – poetry, prose, or an mpeg4 movie.
  Criteria:
    NSI Service typename:
      A string: “ETS” interpreted locally by the PA NSA
      Or a URL pointing to the XML CSD doc: //nsi.nordu.net/ets/CSD
    Generic service parameters:
      Schedule - start date/time, end data/time
      Authorization credentials
      Path object – Source STP, Dest STP, optional EROs
    Service specific parameters e.g.
      <“bandwidth”, 5.0, “Gbps”>
      <“frameErrorRate”, 10^-8, “averageErrorsPerFrame”>
(See WSDL for more formal description)

## Slide 41: The Network Service Agent
A “Network Service Agent” (NSA) is associated with and represents an NSI Network domain:
  The NSA speaks the NSI protocol(s) to other NSAs
  It acts as a Provider Agent (PA) when receiving service requests
  It acts as a Requesting Agent (RA) when it issues requests to other NSAs
  At the leaf nodes, the NSA interacts with a local Network Resource Manager (NRM) to reserve specific network resources (this interaction is NRM specific and not part of NSI standard.)
  NSAs “Aggregators” decompose a request into segments that can then be delegated to other domains
Curacao
Bonaire
Aruba
A
Application NSA
Aggregator NSA
PA
PA
RA
RA
RA
PA

## Slide 42: NSI Request Segmentation
An NSA is free to select the path and the process by which a Connection reservation is established.
An NSA performing inter-domain path selection and reservation may ask other NSAs to perform part of the provisioning
  Thus, an NSA may recursively decompose or “segment” the request into a series of component “children” segments that transit other domains.
  NSI Reservations are then issued to the respective NSAs for each of these children segments
All children segments must be successfully reserved before the end-to-end reservation can be confirmed back to the requesting agent.

## Slide 43: The Service Tree
The resulting recursive structure is called the “Service Tree”
Each Provider NSA may segment a request as necessary to meet the service criteria
  An NSA may delegate all or part of a service request to other NSA(s)
  (Such may be necessary to handle third party requests, federations, or to find necessary resources,…)
Each NSA maps Connection IDs of received connection requests to the Connection IDs of the resulting children segments that make up the end to end reservation.
Domain C
Domain B
Domain A
A
Application NSA
NSI Service Tree
C
B

## Slide 44: The Service Tree
The NSI Service Tree is created for each service request.
The Service Tree is a control plane structure made up of all NSAs involved in processing a single service request
The NSI Service Tree provides a means for the requesting agent to manage a connection end to end through many different downstream providers
And it enables the providers to account for the resources and to have means of properly communicating with the requesting agent responsible for the connection.
C
Domain C
B
Domain B
Domain A
A
Application NSA
NSI Service Tree

## Slide 45: The Service Tree
The NSAs in the service tree are referenced according to their position in the tree :
  Ultimate Requesting Agent “uRA” – the root NSA that originates a request
  Ultimate Provider “uPA” – is a leaf node agent that interfaces directly to the local NRM
  Aggregator – is an NSA that is able to perform inter-domain path segmentation.
C
Domain C
B
Domain B
Domain A
A
Application NSA
NSI Service Tree
uRA
uPA
Aggregator

## Slide 46: Tree and Chain Processing
NSI Framework and the CS protocol support two forms of request processing: “Tree”, and “Chain”
“Chain” segmentation is essentially the conventional hop-by-hop forwarding of the service request downstream towards the destination.
  Inter-domain path selection is performed by each NSA on a hop by hop basis
“Tree” processing allows an external agent to select a sequence of networks for the desired path and then directly contact each network to reserve each segment or cross-connect.
  This is important where delegation of authorization is not honored or is unavailable for chain processing.

## Slide 47: Tree vs Chain Processing
Tree and Chain processing are actually quite similar:
    Chain processing represents a depth-first service tree,
    Tree processing represents a breadth-first approach to path selection.
Tree requires topology/state information to be distributed, which is a major scaling issue…
    But tree also allows more direct relationships between providers and requesters, and with selective topology distribution can provide better macro end-to-end path visibility decisions.
Chain is fast – this is largely due to local authoritative path selection at intermediate transit networks
    Chain only requires reachability information to make path decisions, thus allowing local domains to keep local state local.
    But Chain must delegate authorization criteria, and does not have a global view of the end-to-end network.
NSI allows either or both methods to be used in request processing.

## Slide 48: NSI Connection Segmentation
PA
1
2
3
4
5
6
1
2
3
4
5
6
uRA
PA
PA
A
B
C
D
M
B
C
D
A
B
C
D
Chain model
Tree model
A
Z
A
Z
A
Z
1
2
3
4
5
6
3rd party request
3
4
5
6
1
2
A
B
C
D
7
8
Chain model
Tree model
Chain model
Tree model
Chain model

## Slide 49: NSI-CS Protocol State Machine
Each Connection instance in each NSA has a number of states that must be managed consistently:
  The Reservation state (the selection of a path and booking of resources)
  The Provisioning State (the process of reconfiguring the data plane hardware.)
  The Activation state (the operational state of the connection)
  The Terminating state (the process of freeing up all allocated resources and cleaning up.)

## Slide 50: NSI CS State Transitions
NSA
NSA
NSA
NSA
NRM
NRM
uRA
AGA
uPA
uPA
AG

## Slide 51: NSI State Machines
See Kudoh-san’s presentation ()

## Slide 52: Service Definitions
Service Definitions define the “service” that is being offered.
Within the NSI context, the SD is a machine readable document processed by NSAs that defines the service parameters for the service domain
  NSI Service Typename = “ets” or “LHCONE-P2PCS” or..
  Each service parameter is defined by four elements:
    Parameter Name - a string, e.g. “Capacity”
    Parameter Value - string, real, integer, range, choice,…
    Parameter Units - string, e.g. “bits per second”
    Defaults where appropriate
Service Definitions within NSI are still settling…
  V2 recognizes the service type in the request
  NSAs need to begin validating Request paramters agains service parameters…

## Slide 53: Service Definitions
The Service Definition does *not* describe technically how the connection service is engineered – that is a local engineering decision.
SDs identify the service properties or characteristics that are recognized by the service
  And for each property, the SD describes the allowable limits for that property…for example:
    “Capacity” := from 0 to 100*10^9 units “bits per second”
    “MaximumBurstSize” := 1*10^6 unit “bits”
Service characteristics not explicitly described in the Service Definition are explicitly undefined – i.e. unreliable, non-deterministic, unpredictable, absent, random, ...
  There is no basis for assuming any particular behaviour for undefined service properties

## Slide 54: Service Compatibility
A group of service providers may elect to offer “similar” NSI services. They adopt a Common Service Definition (CSD) that will apply to all conforming service domains:
  Each service domain must recognize all service parameters defined in the CSD (ranges may be locally adjusted…)
  Each service domain defines like Framing and service Payloads for the boundary STPs
In NSI version 2, interconnected service domains are treated as a single contiguous layer
Multi-layering of network technologies is actually a topology processing issue – path finding…not a provisioning issue.
NSI does not stipulate path finding algorithms.
NSI is insensitive to layers – it will work for any service layer.

## Slide 55: Service Definitions
  CSDs can (should!) be refined iteratively over time – adding new service parameters, or even new service types
    Does not require a change to the NSI protocol(s)
SDs may be modified by the service provider at any time.
CSDs may be modified by consensus of the providers
Example: A NSI-CS Reservation request will specify:
  NSI Service typename:
    A string: “ETS” interpreted locally by the PA NSA
    Or a URL pointing to the XML CSD doc: //nsi.nordu.net/ets/CSD
  Generic service parameters:
    Schedule
    Authorization credentials
    Path object
  Service specific parameters e.g.
    <“bandwidth”, 5.0, “Gbps”>
    <“frameErrorRate”, 10^-8, “averageErrorsPerFrame”>

## Slide 56: Questions?
Summary:
  NSI is a Framework
  There is a basic high level global topology model..
  And a set of protocols that work across this model
  NSI Connection Service protocol is first out of the gate…
  Connection Life Cycle
  Service Tree – RAs, Pas, … uRA/uPA/Aggregators
  Service Definitions …

## Slide 57: Exercise #1 Basic Connection Life Cycle

## Slide 58: Exercise #1 Basic Connection Life Cycle
Objective: Demonstrate the ability to set up and utilize a simple NSI testing facility.
This exercise will have the student construct a small NSI network service domain consisting of network infrastructure (a single switch), and NSA (a PC running one of the NSA variants), and two end systems between which connections can be set up and verified.
Students can initiate the Reservation request from the command line tools or a Web GUI.
STPs: ES1-[80..83]
STPs: ES2-[80..83]
Ethernet switch
=RA
PA
NSI CS
NRM
You
Your laptop
NSI Network Service
Domain
NSA
“maui.ets”
NSI Resv.rq: maui.ets:ES1-80 > maui.ets:ES2-80

## Slide 59: Introduction NSI-CS State Machines and the Message Delivery Layer
Understanding the state transitions
How messages are handled by the NSA
Tomohiro Kudoh – AIST, co-chair NSI WG, the smartest guy in the room

## Slide 60: Tomohiro’s Slides

## Slide 61: A Peek at the NSI Web Service Description (WSDL)
The formal software WS specification of the NSI service interfaces
* Inder Monga
Begin Inder’s Slides

## Slide 62: Lunch

## Slide 63: Exercise #2 Multi-Domain

## Slide 64: Exercise #2 multi-Domain Connections
Install NSA
aruba.ets
port7-[80..83]
port7-[80..83]
dominica.ets
bonaire.ets
curacao.ets
port11-[80..83]
Port3-[80..83]
eth-sw1
eth-sw2
eth-sw3
eth-sw4
STPs: port-[80..83]
port12-[80..83]

## Slide 65: Introduction NML Topology for NSI
What is OGF NML (briefly!)
What is “N3” and how does NML fit ?
Topologies, Nodes, Ports, Links.
Bi-dir vs Uni-dir…
Jeroen van der Ham - co-Chair of OGF NML WG and research scientist at UvA

## Slide 66: Jeroen’s Slides

## Slide 67: Exercise #3 Topology Descriptions
Install NSA
aruba.ets
port7-[80..83]
port7-[80..83]
dominica.ets
bonaire.ets
curacao.ets
port11-[80..83]
Port3-[80..83]
eth-sw1
eth-sw2
eth-sw3
eth-sw4
STPs: port-[80..83]
port12-[80..83]
The topo from exercise 2…

## Slide 68: Exercise #3 Topology Descriptions
Install NSA
aruba.ets
port7-[80..83]
port7-[80..83]
dominica.ets
bonaire.ets
curacao.ets
port11-[80..83]
Port3-[80..83]
eth-sw1
eth-sw2
eth-sw3
eth-sw4
STPs: port-[80..83]
port12-[80..83]
… swap relative positions of Cuaracao and Dominica2…

## Slide 69: Introduction Putting It Together
How should the engineering amd management proceed towards NSI deployment?
Jerry Sobieski, et al
Begin Jerry’s Slides

## Slide 70: Getting Started
Set up a test lab
Construct or adopt a Common Service Definition
Define the intra-domain hardware and software engineering
Select the NSA software implementation you will use
Define the NSI inter-domain service topology
Construct or adopt an Authorization Profile
Ancillary Issues: Monitoring, Debugging, Reporting, …
Training (ops/eng staff), & user community (res/dev)
Experiment Deployment – early adopters
“quasi-Production” – 24x7x365, full capacity, early adopters
Production – multiple services, standard offerings, …

## Slide 71: 1. NSI Test Lab - Learning
First objective: Learn the basics of NSI configuration
Assume a simple Ethernet Transport Service to get started...
Hardware: One switch. Several is step 2 …
  MPLS router – will need ethernet encapsulation into LSPs- typically better support for BW policing/shaping
  Ethernet hardware can be used – but it poses technical problems for WAN application (mac flooding, flat VLANs, limited VLANs, …) – prefer 802.1Q (tagging) capability, VLAN swapping is *highly* desirable, …
  SONET/SDH hardware can be useful – requires a ethernet to GFP encapsulation, GFP-T is preferred over GFP-F.
  NOTE: The NSA software will need to interface with your particular brand/type of hardware or software NRM. So check with the NSA software for compatible “southbound” interfaces.
Other Hardware:
  NSA server – check with the NSA software for OS compatibility
  End system PCs – almost anything that can set up IP interfaces and ping

## Slide 72: 2. Find a common “NSI service” community
The “local” network management must decide on a Service Definition that they wish to offer.
NSI can support many types of connection services
An NSI network service – by definition – is part of a global community of similar services
So… The “local” network management must find or organize the community to develop a Common Service Definition
Some such communities are already forming:
  GLIF – Automated GOLE “ethernet transport service”
  LHCONE - developing a “point to point connection service”

## Slide 73: Construct or adopt a Service Definition
The Service Definition is a formal description of the commitment the Provider will be making to users in terms of service guarantees
The Common Service Definition is a starting point
  It describes the minimum capabilities that the service must offer
  And the parameters that will be used to request services
The local management may modify the service offering in certain ways
  Typically, to expand or limit the range of service instances
  But the resulting Local Service Definition must remain compatible with the CSD

## Slide 74: 3. Lay out your intra-domain engineering
Start with a single “domain” – define the STPs.
  As a “uPA” you won’t need to advertise them… but know them internally by the NRM
Identify the hardware you will use for your test infrastructure inside your domain
    Ethernet switch? Router? SONET/SDH/OTN?
Which NSA software has drivers for this hardware?…or plan to write an interface module (easy)

## Slide 75: 4. Select the software
This is largely a matter of evaluating the package for support and easy of configuration and mgmt
Identify the hardware you will use for your test infrastructure inside your domain
    Ethernet switch? Router? SONET/SDH/OTN?
Which NSA software has drivers for this hardware?…or plan to write an interface module (easy)

## Slide 76: NSI Test Lab – Software Evaluation
Objective: Software Evaluation. Decide which software you will want to use in your production NSI Connection Service
You will want to evaluate several NSI software implementations
Which provide the functionality your user community will want you to offer?
  … Some do not offer aggregator capability – do you view “one stop shopping” as a functional requirement for your user community?
  … Some may offer hardware interface modules for your hardware. Or not...
You may decide to add an NSI front-end/wrapper to your own network management system
  Requires software development up front, but then it integrates with existing operational processes and systems…
How easy/reliable is it to install and configure the NSA software?
  Your network engineering staff will be responsible for this… Do they need to be web service developers or can it be done by conventional network engineering skill sets?
It is also necessary to understand the software support issues:
  Who will be supporting your production software? i.e. fixing bugs, adding features, etc?
  How easy would it be for your staff to support an open sourced version of your chosen software? Is there a process for managing community based development?

## Slide 77: 5. Lay out your test domain
Start with a single “domain” with several STPs.
  As a “uPA” you won’t need to advertise them… but know them internally by the NRM
Plan stage 2: Another domain – in the lab initially – that you can set up the SDPs between the test domains
  At this point, you will want to test:
    a) the uRA tree segmentation across the two domains
    B) the aggregator function in one or both NSAs to perform path finding
  The PF aspect will require N3 topology descriptions for each domain made available to the other
    Monitor the evolution of NSIv3 regarding a topology service for exchanging topo info… or place the topo files online (for now) where the NSAs can reach them
Plan a collaborative field test with another adjacent network…
Join the Automated GOLE project – ideal for a test deployment.

## Slide 78: Introduction The GLIF Automated GOLE
What is the GLIG AutoGOLE facility?
* Jerry Sobieski NORDUnet Director for Int’l Research, TL for the GLIF AutoGOLE Pilot, co-Chair of GLIF Performance Verification Architecture Task Force, formerly with MAX (US)
Begin Jerry’s Slides

## Slide 79: The GLIF Automated GOLE Pilot Project

## Slide 80: Automated GOLE Fabric
PSNC
JGN-X
NetherLight
Cern
UvA
CzechLight
KRLight
AIST
KDDI Labs
StarLight
GLORIAD
GEANT
ACE
Nordunet
CANARIE
ESnet
Pionier
US LHCnet
The GLIF Automated GOLE global fabric

## Slide 81: What is the AutomatedGOLE “Fabric”?
The Automated GOLE fabric includes many facilities:
  Exchange Points (& “distributed” facilities)
  Inter-exchange transport links
  Networks
    GOLEs link networks together …
  Organizations that are willing to contribute people, facilities, hdw/sfw, etc.
  Users/applications entities
  …

## Slide 82: Automated GOLE + NSI
Pionier
AutoBAHN
POZ
StarLight
OpenNSA
CHI
AIST
G-LAMBDA-A
Tsukuba
NSIv2 Networks and Exchange Points
NSI peerings (SDPs) unless otherwise indicated these are vlans 1780-1783
KRLight
DynamicKL
DAE
KDDI-Labs
G-LAMBDA-K
Fujimino
ACE
KRLight
JGN-X
JGN-X
G-LAMBDA-K
TOK
CzechLight
OpenDRAC
PRA
ESnet
OSCARS
Planned/peerings (SDPs)
GEANT
BoD
GLORIAD
OpenNSA
Network
SC12
Salt Lake City
Ethernet Transport Service
NORDUnet
OpenNSA
Network
PSNC
AutoBAHN
POZ
CESNET
GEANT
A
NSIv1 Networks and Exchange Points
A
Joint NSI v1+v2 Beta Test Fabric Nov 2012
A
UvA
OpenNSA
AMS
A
A
A
NetherLight
OpenDRAC
AMS
US-LHCnet
OSCARS

## Slide 83: Automation by NSI:
Software Implementations
  OpenNSA – NORDUnet (Copenhagen, DK)
  OpenDRAC – SURFnet (Amsterdam, NL)
  G-LAMBDA-A - AIST (Tsukuba, JP)
  G-LAMBDA-K – KDDI Labs (Fujimino, JP)
  AutoBAHN – GEANT (Poznan, PL)
  DynamicKL – KISTI (Daejeon, KR)
  OSCARS – ESnet (Berkeley, US)
Hardware/NRMs covered:
  Juniper / “JunOS” : L2 & MPLS provisioning - OpenNSA
  Brocade: L2 switching - AutoBAHN, OpenNSA
  Ciena (Nortel) SDH & L2 switching – OpenDRAC
  Dell L2, NTT optical: G-LAMBDA-A
  Force10: L2 switching – OpenNSA
  Argia: L2 Switching - OpenNSA
  Ciena NMS – DRAC (TBD)

## Slide 84: Initial monitoring & visualization
“Automated Earth” viz
(Takatoshi Ikeda, KDDI-Labs)
“Status Monitor” viz
(Tomohiro Kudoh, AIST)

## Slide 85: Pointers
Visualization
AIST Java status monitor: http://163.220.30.174:8070/monitor.jnlp
KDDI Labs Google earth plugin: http://kote-ps-1.ps.jgn-x.jp/ps/autoearth-nsi/
KDDI Labs Google earth kml: http://kote-ps-1.ps.jgn-x.jp/ps/autoearth-nsiAutoMAP.kml

## Slide 86: Discussion, other topics, closing
The End
The End

## Slide 87: NSI Development & Road Map
OGF NSI-CS version 2.0 is in draft now (Jan 2013)
Version 2 implementations are under development:
NSI v2 Engineering Workshop to be presented at TIP 2013 (Jan 2013)
First production services planned for 2013:
  NetherLight
  StarLight
  NORDUnet
  GEANT
These will use Version 2

## Slide 88: NSI Development and Roadmap
The OGF NSI WG is chaired by an International set of co-chairs:
  Guy Roberts (DANTE)
  Inder Monga (Esnet)
  Tomohiro Kudoh (AIST)
Work will proceed in 2013 to address “Operationalization” of NSI
  Chaired by Inder Monga (Esnet) and John MacAuley (SURFnet)
  Service Definitions, AAI profiles, Monitoring, …
The GLIF Automated GOLE Pilot Project will continue to provide a global testbed
  Chaired by Jerry Sobieski (NORDUnet)->Gerben van Malenstein (SURFnet)

## Slide 89: NSI Version 3
Work will begin to define NSI v3 capabilities in early spring 2013
The WG will begin taking requirements and issues after TIP
Topics that will likely be on the agenda:
  Topology Service – scalable distributed topology management
  Session management – address NAT/FW issues better, MTL,…
  P2MP
  Automated Performance Verification Service
  Simplify state machines – revisit Modify() to integrate better

## Slide 90: Advanced NSI Topics: NSI+SDN
SDN is about switching and forwarding.
SDN assumes there is a transparent “pipe” between the interfaces of the switching/forwarding Nodes
NSI provides transparent “pipes” between end points, globally.
NSI – expressing transport requirements across multiple administrative service domains - is an inter-domain technology
SDN – controlling the fundamental forwarding behaviour of network hardware - is an intra-domain technology
NSI + SDN - are complementary technologies
SDN can be utilized intra-domain by the NRM to establish a “pipe” (or flow) across the domain interior.
NSI can be utilized inter-domain by the NSA to communicate the end-to-end requirements for the “pipe” to other domains.
NSI can also be utilized as the mechanism whereby physically separated domains with arbitrary internal technologies and systems may establish a “pipe” across the inter-domain medium in order to create a virtual adjacency between these domains.
NSI SDN

## Slide 91: NSI as inter-Domain Transit Services
The inter-domain transport model:
  NSI-CS is used to establish transparent conduits between SDN domains.
  These Connections create SDN adjacencies over/thru intervening multi-layer transit networks
    The NSI domains are opaque - they just provide the basic atomic network function of transparent transport links.
  This model recognizes real world MAN/WAN transport engineering issues
X
CP
X
X1
CP
X2
NSA
NSA
NSI Enabled
SDN Controller
Intervening opaque
NSI transport domains
NSI
NSI
NSI
No change internally
to the SDN architecture or operation
The SDN environments are topologically adjacent by merit of
NSI established transparent connections

## Slide 92: SDN transit technology with NSI inter-Domain
The SDN based transit network service model:
  NSI-CS is used to provision connection requests across an SDN environment.
  This model allows NSI-CS to offer SDN flow spaces via the n-tuple STP mapping.
    Enables “flow space defined” transport links connections.
    It is consistent with NSI abstractions (domain boundaries, STPs, etc.)
X
CP
X
X1
CP
X2
NSA
NSA
NSI peer network
Transit networks using SDN
Technologies internally
NSI
NSI
Independent
NRM
NSI is used as the east/west interface across SDN domains to establish end-to-end connectivity
NSA
Integrated
NRM
X1
X2
X3
X1
X2
X3
NSI peer network
NSI
NSI transit networks

## Slide 93: SDN Slicing using NSI for inter-Domain Adjacencies
The SDN control agents dynamically construct global slices using NSI to provision link slivers across the inter-domain global medium
Y
Ctlr
Y
Y
X
X
Ctlr
NSA
NSI request for links pipes beween Blue slivers
NSI request for a link between Green slivers
Contiguous NSI
metro/regional/longhaul
transport networks
NSA
NSA
GreenX Slice
BlueY Slice
North Carolina
Maastricht
Milano
OpenFlow
Blue slice
OpenFlow
Green slice

## Slide 94: Advanced NSI Topics: Composable Services
Composable Service Capabilities
  Not all issues will become explicit NSI protocol functions –
  many will be addressed by constructing sophisticated higher functions from atomic protocol primitives and intelligent processing/analysis of the information so acquired:
    Optimized workflow scheduling
    Virtualize
  Service design
    Virtual services (NSI services constructed from resource pools made up of other NSI service instances.)
    NSI + SDN
  Path Finding and Topology
    Diversity and Redundancy engineering
    Negotiation and
    Multi-service adaptation

## Slide 95: Advanced Topics: Negotiated Services
Ability to optimize a service instance based upon user defined parameters
    NP complete problem…only the PA has authoritative state,
    And only PA has authoritative control of resources…
    So an RA wishing to optimize a service instance must either a) present the optimization criteria to the PA, or b) the RA must be able to access and analyze the global topology state itself
    Where the RA is optimizing a group of connection requests – they become dependent upon one another…
Some aspects of negotiated services are higher layer functions that a PA is unable to resolve (nor is the PA the appropriate agent to make optimization decisions for a HEP app or a VLBI ap, etc.)

## Slide 96: Advanced Topics: Multi-Service NSI Environments Tunneled Adjacency
S
S
S
S
S
E
E
E
Aruba.EFTS
Curacao.TDMS
The physical infrastructure
layer
Aruba.TDMS
S
S
S
Bonaire.TDMS
NRM
NRM
E
E
E
NRM
The “TDMS”
NSI service layer
The “EFTS”
NSI service layer
Aruba
Bonaire
Curacao
Bonaire.EFTS
A1
S1
S2
S4
S5
A2
B1
B2
A3
B3
S3
S6
Pre-Engineered GFP adaptation. Not announced in topology
NSI Provisioned [SDH] Tunnel Connection
Announced SDP adjacency

## Slide 97: Advanced Topics: Multi-Service NSI Environments Transit Service
S
S
S
S
S
E
E
E
Aruba.EFTS
Curacao.TDMS
The physical infrastructure
layer
Aruba.TDMS
S
S
S
Bonaire.TDMS
NRM
NRM
E
E
E
NRM
The “TDMS”
NSI services
The “EFTS”
NSI services
Aruba
Bonaire
Curacao
Bonaire.EFTS
A1
S1
S2
S4
S5
A2
B1
B2
A3
B3
S3
S6
Static Engineered GFP adaptation
NSI Provisioned [SDH] Tunnel Connection
Curacao.EFTS
C1
C2
SDP
SDP

## Slide 98: Advanced Topics: Multi-Service NSI Environments Explicit “stacking” Adaptation
S
S
S
S
S
E
E
E
Aruba.EFTS
Curacao.TDMS
The physical infrastructure
layer
Aruba.TDMS
S
S
S
Bonaire.TDMS
NRM
NRM
E
E
E
NRM
The “TDMS”
layer
The “EFTS”
layer
Aruba
Bonaire
Curacao
Bonaire.EFTS
A1
S1
S2
S4
S5
A2
B1
B2
A3
B3
S3
S6
Static Engineered GFP adaptation, but announced as Service Adaptation Points
SAP
(A3,push,GFP,S2)
SAP
(S6,pop, GFP,B3)
SDP
SDP

## Slide 99: Advanced Topics: Multi-Service NSI Environments Hidden “swapped” Adaptation
S
S
S
S
S
E
E
E
Aruba.EFTS
Curacao.TDMS
The physical infrastructure
layer
Aruba.TDMS
S
S
S
Bonaire.TDMS
NRM
NRM
E
E
E
NRM
The “TDMS”
NSI service layer
The “EFTS”
NSI service layer
Aruba
Bonaire
Curacao
Bonaire.EFTS
A1
S1
S2
S4
S5
A2
B1
B2
A3
B3
S3
S6
Static engineered GFP adaptation, but announced as SDP with no technical specifics
SDP
(A3,S2)
SDP
(S6,B3)
SDP
SDP
Service Payload must be very clearly defined in all service domains in order to strip ingress framing and replace it with native transport framing. Likewise, transport framing is stripped and replaced with egress framing .

## Slide 100: OGF NSI Working Group
The OGF NSI WG is an Open working group
This means if you have ideas you would like to see incorporated into the NSI framework and/or protocols, please get active in the process:
    Contact one of the active WG members and pick their brain, learn the current architecture
    Join the mailing list, lurk and get up to speed, then join the calls…
    Contribute – ask, comment, propose…help us sort thru the issues to achieve clarity within the group and consensus within the broader global community
Thank You!