## Slide 1: Introduction to Connection Oriented Concepts
Inder Monga
Chief Technologist, ESnet
Co-chair, NSI working group
NSI Tutorial @ TIP 2013
January 13th

## Slide 2: Lambdas and Lightpaths
Lambda
  Wavelength or a physical circuit
Lightpath
  Communications channel aka virtual circuit
  Connects two points in the network
  Has capacity associated with it
  Technology agnostic, multiple ways to build a circuit
5 Gbps
Lightpath
Network Aruba
Network Curacao

## Slide 3: Myth Busters
Bandwidth:
  Maximum capacity of a given lightpath/lambda
Throughput:
  How many application bits/second can get carried between any two points of the network
10
Gbps
100
Gbps
Network property
Application or end-to-end property
From my.es.net
Notes: Network as a water pipe, Bandwidth is the maximum water flow

## Slide 4: On-Demand
Bandwidth, not throughput
“On-demand” is defined by time-scale
  Not O(days or months)
  But O(seconds to minutes)
Additional property
  Software-controlled
  GUI or Application initiated

## Slide 5: Some more truths
Application can try engineer their end-to-end throughput
Application currently can request point-to-point bandwidth
  As supported in many installations today
  Focus of first protocol of NSI framework
  Point-to-multi-point investigated
Throughput ? Bandwidth
  !=
  ≤
100 Gbps
Application A
12 Gbps
Application B
28 Gbps
TCP congestion performance

## Slide 6: “Guaranteed” Bandwidth
ESnet
NERSC
BNL
Bandwidth reserved for a single flow or set of application flows (or lightpath)
  Edge-to-edge
  End-to-end
Related concepts
  Best Effort
    Public Internet
  Oversubscription
    Aggregation
Notes: Look for appropriate images

## Slide 7: Styles of Guarantee
Dropped
2Gbps max
Strict or exact
  Ceiling
  Peak
Floor
  Traffic above floor marked for discard if congestion
t 
1Gbps floor
Marked
but not
dropped
Guaranteed
t 

## Slide 8: Domains (networks)
Administrative boundaries are broad and can be arbitrary
Single Domain
  Single administrative management entity
Multi-domain
  Multiple administrative management entities
ESnet
USLHCnet
CERN
BNL

## Slide 9: BoD Spans Network Layers
Layer 3/2.5: MPLS
Layer 2: Carrier Eth.
Layer 1: Lightpath/OTN
Layer 0: Wavelength

## Slide 10: Scheduling
On-Demand
  Time: Now
  Duration: Till when I please
Scheduled
  Time: Start-time, specific time in the future
  Duration: End-time OR time duration

## Slide 11: Reservation
Network Resources reserved for a certain application at a certain “schedule”
  Bandwidth, Path
On-demand is equivalent to instant bandwidth reservation with no specified end-time

## Slide 12: Path-Finding
Two ends of the network
  Start = A point
  End = Z point
Path
  Creating a physical or virtual circuit between points A and Z passing through multiple network devices
Can be single or multi-domain
Multi-layer path-finding a lot more complex than at a single layer
ESnet
USLHCnet
CERN
BNL
A
Z

## Slide 13: Unidirectional vs. Bidirectional paths
Most protocols are bidirectional but may not require symmetric reservations
  Example: Large data transfer
Two kinds of bidirectional:
  Associated
    Two unidirectional paths
    Complex management, since independent entities
    May follow different routes
  Co-routed
    Forward and backward follow the same route
    Usually setup as part of a single operation
    Transport paths are typically co-routed

## Slide 14: Topology
Map of interconnected devices
  Intra-domain
  Inter-domain
Network and technology characteristics
Can represent the physical layer limitations
Notes: What’s possible

## Slide 15: Topology (contd.)
Virtual topologies refer to logical connections or limited subsets of the physical topology
Physical topology is the most straightforward
  Which port, node, location, etc.

## Slide 16: Path Computation Engine (PCE)
Choose a path based on Topology, current network state and certain criteria
Current network state
  Available capacity and resource commitments
  Includes reservations in the future
Criteria
  Bandwidth
  Layer
  Latency
  Green energy
  Your favorite metric

## Slide 17: Modify
Ability to change certain parameters of the reservation
  May or may not cause service outage
  Focus on a very limited set of parameters
Modify can be powerful for applications facing a varying workload
  Can only be implemented at Layer 2 or above in the network
  Duration is typically the most modified parameter where the connection remains the same
  Bandwidth is the next most common

## Slide 18: Bandwidth vs Connection on-Demand
Bandwidth-on-demand does not have to mean a new connection setup
  ~0 bandwidth circuits
  Use modify to add bandwidth, if available
Connection-on-demand is what most of us refer to as BoD
  Provisioning and teardown of new connections are more resource intensive
Question – What suits your purpose?

## Slide 19: Limitations

## Slide 20: Physical Infrastructure
Most applications not familiar with the topology might assume BoD capabilities that is not physically possible
  For example:
    40G NIC on application host, 10G WAN connectivity of DC
    Can’t do 40G flows over nx10G connectivity

## Slide 21: Site Network Architecture Science DMZ design patterns
Data Site
Supercomputer Center
Science DMZ
Abstract Design

## Slide 22: Blocking
‘Guaranteed Reservations’ of other applications might consume all resources
  Even though the traffic profile indicates a lot of headroom
Some of these reservations might be scheduled
  Similar to hotel reservation
An intermediate network domain might have resource constraints
  Path finding needs to be intelligent
  Path computation may take a lot of cycles if networks are ‘reservation congested’

## Slide 23: Putting it all together
Multi-layer, multi-domain, multi-vendor, On-Demand, Bandwidth Scheduling and Reservation Service
Service is the most important aspect, protocols only are building blocks

## Slide 24: What else is needed for a service?
Authorization and Authentication, Trust
  Global federated system that works well with applications
Service Level Agreements
  What is the lowest common denominator across the multi-domain network?
Service Definition
  Consistent view of the end-to-end service
  Homogenous service over heterogeneous technologies
Monitoring and measurement
  End-to-end as well
Multi-domain debugging
  How do you find errors, report them so they can be debugged and fixed?

## Slide 25: Top to Bottom view
Data Plane:
carries real bits, electrical and optical
Control Plane:
distributed management of forwarding
Management Plane:
Provisioning and management of the network devices and as a system
Service Plane:
End-to-end services, application-oriented
NSI

## Slide 26: Questions?
Imonga at es.net

## Slide 27: Network Services Interface
Standards process in OGF
Strong participation from NREN community
Notes: Unproven in scale, AutoGOLE, Topology

## Slide 28: Network Service Framework concepts
Service Plane
Service
Requestor
Service
Provider
Network Services Interface (NSI)
NSI Requestor
Agent (RA)
NSI Provider
Agent (PA)
NSA
NSA
Network Service A
Network Service B
Network Service A
Network Service B
NSA = Network Services Agent
NRM = Network Resource Manager
Local Resources
NRM
NRM
Local Resources
Transport Plane
* Slides contain animation, does not show in pdf
Notes: 1. Connection Service, a service used to request and manage transport connections. Another example is the Topology Service; this is used to exchange network topologies.